## Slide 1: Properties of the Fourier Transform
Based on the video lecture

## Slide 2: Reminder: Definition of Fourier Transform
Given a signal x(t), its Fourier Transform is:
X(ω) = ∫_{-∞}^{∞} x(t) e^{-jωt} dt
Inverse Fourier Transform:
x(t) = (1/2π) ∫_{-∞}^{∞} X(ω) e^{+jωt} dω

## Slide 3: Main Properties We Will Cover
1) Linearity
2) Time Shift (shifted signals)
3) Modulation / Frequency Shift
4) Convolution
5) Derivative (and N-th derivative)
6) Duality

## Slide 4: Property 1: Linearity
If we have a linear combination of signals:
α₁ x₁(t) + α₂ x₂(t)
Then the Fourier Transform is the same combination:
α₁ X₁(ω) + α₂ X₂(ω)

## Slide 5: Proof of Linearity (as in the video)
F{α₁x₁(t) + α₂x₂(t)}
= ∫_{-∞}^{∞} [α₁x₁(t) + α₂x₂(t)] e^{-jωt} dt
Use linearity of the integral:
= α₁ ∫ x₁(t)e^{-jωt} dt + α₂ ∫ x₂(t)e^{-jωt} dt
Recognize transforms:
= α₁ X₁(ω) + α₂ X₂(ω)

## Slide 6: Property 2: Time Shift
Consider a shifted signal:
x(t - t₀)
Fourier Transform becomes:
F{x(t - t₀)} = e^{-jωt₀} X(ω)

## Slide 7: Proof of Time Shift (as in the video)
F{x(t - t₀)} = ∫ x(t - t₀) e^{-jωt} dt
Rewrite exponential:
e^{-jωt} = e^{-jω(t - t₀)} e^{-jωt₀}
Bring constant outside:
= e^{-jωt₀} ∫ x(t - t₀) e^{-jω(t - t₀)} dt
Change variable τ = t - t₀, dτ = dt:
= e^{-jωt₀} ∫ x(τ) e^{-jωτ} dτ
Recognize transform:
= e^{-jωt₀} X(ω)

## Slide 8: Property 3: Modulation / Frequency Shift
If a signal is multiplied by a complex exponential:
e^{jω₀t} x(t)
Then its spectrum shifts:
F{e^{jω₀t} x(t)} = X(ω - ω₀)

## Slide 9: Property 4: Convolution
If two signals are convolved in time:
x(t) * y(t)
Then in frequency we get multiplication:
F{x(t) * y(t)} = X(ω) Y(ω)
This is one of the most important properties.

## Slide 10: Property 5: Derivative
First derivative:
F{dx(t)/dt} = jω X(ω)
General N-th derivative:
F{dⁿx(t)/dtⁿ} = (jω)ⁿ X(ω)

## Slide 11: Property 6: Duality
If we have a transform pair:
x(t) ↔ X(ω)
Then we get another pair for free:
X(t) ↔ 2π x(-ω)
Knowing one pair gives you another one.

## Slide 12: Closing Remark
These are the key Fourier Transform properties you need to master.
Their proofs are straightforward applications of integral properties.
Practice proving them to become familiar with the Fourier integral.